## Slide 1
DIGITAL ELECTRONICS
Design & Simulation of 8-Bit Signed Binary Number Representation
Using One’s Complement Method
A simple look at how computers represent positive and negative numbers.
8-BIT
0
1
0
0
1
1
0
1
SIGN
0 = + 1 = −
Presented by: Anagha Nagaraj Kuruvinkopp CSE – 1st Year | KL University, Hyderabad

## Slide 2
Why Do We Need Signed Numbers?
2
WITHOUT A SIGN
Unsigned Binary
00000000 → 0 00000001 → 1 01111111 → 127
Only non-negative values
WITH A SIGN
Signed Binary
＋
positive
−
negative
One’s Complement is one method for representing both.

## Slide 3
An 8-Bit Number Has 8 Positions
3
SIGN BIT
0
b7
1
b6
0
b5
0
b4
1
b3
1
b2
0
b1
1
b0
0 in MSB
Positive number
1 in MSB
Negative number
Remaining bits
Store the magnitude
MSB = Most Significant Bit

## Slide 4
One’s Complement: Flip Every Bit
4
To represent a negative number, complement each bit of its positive binary form.
+13
0
0
0
0
1
1
0
1
↓
0 ↔ 1
−13
1
1
1
1
0
0
1
0
3 EASY STEPS
• Write the 8-bit positive value
• Invert every bit
• The result is the negative value

## Slide 5
8-Bit One’s Complement Range
5
−127
−1
−0 / +0
+1
+127
Positive
0 to +127
Negative
−127 to −0
Important
Two zeros
Overall range: −127 to +127

## Slide 6
Design & Simulation in Logisim
6
1
INPUT
Decimal
→
2
CONVERT
8-bit binary
→
3
CHECK
Sign bit
→
4
INVERT
NOT gates
→
5
OUTPUT
8-bit result
SIMULATION IDEA
For each bit, a NOT gate flips 0 → 1 and 1 → 0.
Example: 00001101 → NOT gates → 11110010

## Slide 7
Examples & Final Takeaway
7
+5
00000101
−5
11111010
+13
00001101
−13
11110010
+25
00011001
−25
11100110
REMEMBER
Negative = invert every bit
One’s Complement is simple, visual, and easy to simulate.
Thank You!