## Slide 1
RISC-V Custom Instruction Candidate Selection
A systematic method for turning workload bottlenecks into efficient ISA extensions
Computer Architecture • ISA Design • Hardware/Software Co-Design

## Slide 2
Why Custom Instructions?
2
Performance
Collapse frequent multi-instruction sequences into one operation, reducing instruction fetch, decode, and execute overhead.
Energy
Fewer instructions and shorter execution time can reduce dynamic activity and memory traffic.
Specialization
Add only the operation the workload needs instead of redesigning the entire processor.
Core idea
Custom ISA design is not about inventing instructions at random. The goal is to identify a workload pattern where the expected system-level benefit clearly outweighs implementation cost.

## Slide 3
Where Do Candidate Instructions Come From?
3
Hot Loops
Use profiling to find loops responsible for a large share of total execution time. Candidates inside these loops have the highest leverage.
Repeated Sequences
Search for instruction patterns that occur repeatedly and can be fused into one semantic operation.
Domain Operations
Cryptography, DSP, image processing, compression, ML kernels, and signal processing often expose strong custom-instruction opportunities.
Compiler Patterns
Look for idioms that compilers already recognize, or operations that require awkward instruction sequences on the base ISA.

## Slide 4
Candidate Selection Workflow
4
01 Profile
Measure workload hotspots
02 Extract
Find repeated computation patterns
03 Model
Estimate instruction/cycle savings
04 Design
Map operation to datapath
05 Evaluate
Area • power • timing • speedup
06 Validate
Benchmark software + RTL

## Slide 5
Key Metrics for Ranking Candidates
5
Frequency
How often does the pattern execute? High frequency increases total benefit.
Instruction Reduction
How many base instructions can one custom instruction replace? Larger reduction generally means more opportunity.
Latency
Can the custom operation finish within the target cycle time, or does it create a multi-cycle/critical-path problem?
Area
Estimate added logic, routing, register-file pressure, and control complexity.
Energy
Consider switching activity, memory traffic, and execution-time reduction.
Software Cost
Compiler support, intrinsic APIs, code generation, ABI impact, and portability matter.

## Slide 6
A Simple Quantitative Ranking Model
6
A practical scoring function can combine benefit and implementation cost:
Score = w₁·F + w₂·R + w₃·S − w₄·A − w₅·P − w₆·C
F — Frequency
Normalized execution frequency of the candidate pattern.
R — Reduction
Estimated instructions or cycles eliminated.
S — Speedup
Expected workload-level performance improvement.
A = area • P = power/energy • C = software + verification complexity • wᵢ = project-specific weights

## Slide 7
Worked Example: Fused Multiply-Accumulate Pattern
7
Baseline sequence
load → multiply → add → store (repeated inside a hot loop)
Candidate custom operation
MAC rd, rs1, rs2 One semantic operation replaces a repeated sequence.
Potential Benefit
Lower instruction count and potentially fewer pipeline stages for the operation.
Hardware Question
Can the multiplier + adder meet timing and integrate cleanly with the datapath?
Validation
Compare CPI, execution time, area, frequency, and energy against the baseline.

## Slide 8
RISC-V Integration Considerations
8
• Use the RISC-V custom opcode space for non-standard instructions.
• Define operand semantics precisely: source registers, destination register, immediates, and side effects.
• Specify exceptions, memory behavior, privilege interactions, and precise-state requirements.
• Keep the extension orthogonal where possible so existing software remains understandable.
Encoding
Choose an encoding that is easy for decode logic and compiler backends to generate.
Pipeline
Check hazards, forwarding, structural conflicts, and whether the instruction is single- or multi-cycle.
Toolchain
Assembler → compiler intrinsic → benchmark → debugger/simulator support.

## Slide 9
Hardware–Software Trade-Offs
9
Choose a candidate when…
• It occurs in a dominant workload hotspot. • It replaces enough work to matter. • It maps naturally to existing or modest extra hardware. • Its latency fits the pipeline strategy. • Compiler/software support is realistic. • Verification effort is manageable.
Reject or redesign when…
• The pattern is rare. • Speedup is small but hardware cost is large. • It lengthens the critical path. • It introduces difficult memory/exception semantics. • It requires extensive compiler changes. • A standard RISC-V instruction already solves the problem efficiently.

## Slide 10
Validation: From Idea to Evidence
10
Software
Instrument and profile real workloads.
Model
Estimate cycle savings and bottleneck movement.
RTL
Implement and simulate functional correctness.
Synthesis
Measure area, timing, and power proxies.
Benchmark
Compare baseline vs. extension across representative inputs.

## Slide 11
Example Candidate Ranking
11
Candidate | Frequency | Instr. Saved | Area Cost | Timing Risk | Decision
Fused MAC | Very High | High | Medium | Medium | Strong
Bit-field pack | High | Medium | Low | Low | Strong
Rare transform | Low | High | High | High | Reject
Crypto round | Very High | Very High | High | Medium | Domain-specific
Ranking is workload-dependent: a candidate that wins for DSP may lose for general-purpose applications.

## Slide 12
Key Takeaways
12
The best custom instruction is not the most complex one — it is the one with the best system-level return.
• Start with real workload profiling, not hardware intuition.
• Prioritize frequent patterns that eliminate substantial instruction or cycle overhead.
• Evaluate performance together with area, timing, power, verification, and toolchain cost.
• Validate the complete hardware/software stack before committing the extension.
• Use quantitative ranking to make the architecture decision explainable and repeatable.
RISC-V custom instructions → workload insight → measurable acceleration → validated architecture